## Slide 1
PROBLEM STATEMENT · DEVS EVALUATION 15%
Micro-Drift Kills Batches
Before Anyone Notices
The Problem
Undetected pH, DO, temperature & OD600 drift silently degrades fermentation and bioprocess yield
The Stakes
A single missed drift event can void an entire high-value biopharma or enzyme production batch
The Gap
Legacy monitoring systems are imported, costly, and rarely deployed below pilot-plant scale
Target Users
Biopharma QC labs, fermentation R&D units, vaccine/enzyme facilities, agri-biotech startups
PARAMETERS AT RISK
pH
±0.2 drift = failed batch
Temperature
±2°C alters growth rate
Dissolved O₂
Anaerobic stress risk
OD600
Biomass curve blind spot
$3,000–$10,000
typical cost of an imported bioprocess telemetry system — out of reach for most Indian labs
BIOSENSE-EDGE | DEVS 2026
1
Notes: Bioprocess batches are exquisitely sensitive — a pH swing of 0.2 or a two-degree temperature drift can silently destroy days of fermentation and lakhs of rupees in raw material. Today's monitoring options are either manual, slow, or imported systems costing three to ten thousand dollars — putting real-time protection out of reach for most Indian biotech labs and university facilities. BioSense-Edge targets exactly that gap: precision, deterministic monitoring for teams that can't justify an $8,000 import.

## Slide 2
SYSTEM ARCHITECTURE · DEVS EVALUATION 25%
Dual-MCU Architecture: Determinism Meets Connectivity
STM32H743ZIT6 — Main MCU
Deterministic Real-Time Domain · 480 MHz
High-Speed ADC/SPI Sampling
Synchronized acquisition across all 4 sensor channels
Closed-Loop PID Engine
Real-time correction with hard timing guarantees
Local SD Black-Box Logger
Zero data loss, independent of network state
ESP32 — Network Co-Processor
Connectivity Domain · Fully Offloaded
Wi-Fi / MQTT Stack
Primary telemetry uplink to cloud dashboard
SX1276 LoRa Fallback
Automatic reroute when Wi-Fi is unavailable
Command Relay
Cloud/dashboard setpoints passed back to PID loop
UART / SPI
Why Split the Load? The real-time control loop never blocks on network jitter, MQTT congestion, or a dropped Wi-Fi connection — hard timing guarantees stay hard, no matter what the network is doing.
BIOSENSE-EDGE | DEVS 2026
2
Notes: We deliberately split compute across two processors rather than one. The STM32H7 owns a hard real-time domain — sampling, PID control, and logging — completely isolated from network variability. The ESP32 handles all the unpredictable stuff: Wi-Fi negotiation, MQTT publishing, and LoRa fallback — so a dropped Wi-Fi packet never causes a missed PID cycle or a pump that doesn't fire on time.

## Slide 3
HARDWARE & SIGNAL CHAIN · DEVS EVALUATION 25%
Lab-Grade Sensing, Galvanically Isolated
pH Probe → Atlas EZO-pH
Lab-grade accuracy over I2C, temp-compensated
DO Probe → Atlas EZO-DO
Dissolved oxygen for aerobic process control
PT100 RTD → MAX31865
Industrial ±0.5°C precision temperature driver
OD600 Sensor
Photodiode-based biomass / turbidity tracking
ISO1540 GALVANIC ISOLATION
Analog / Probe Domain
Ground loops · ESD · pump/heater EMI · wet-probe noise
Digital / MCU Domain
Clean I2C bus into STM32H7 — sensor faults cannot propagate back to probes
BIOSENSE-EDGE | DEVS 2026
3
Notes: Every probe on this rig is lab-grade: Atlas Scientific EZO circuits for pH and dissolved oxygen, a PT100 RTD through a MAX31865 driver for temperature, and a dedicated OD600 photodiode for biomass tracking. But the detail that matters most here is isolation — ISO1540 galvanic isolators sit between every analog probe and the MCU, so ground loops and electrical noise from pumps and heaters never corrupt a sensor reading.

## Slide 4
METHODOLOGY & FAIL-SAFE ROUTING · DEVS EVALUATION 20%
Closed-Loop Control With Built-In Fail-Safes
1
SENSE
All 4 parameters sampled at high speed via isolated ADC/SPI
2
COMPUTE
STM32H7 runs real-time PID correction against setpoints
3
ACTUATE
SSR heating + dual peristaltic acid/base pumps respond
4
LOG
Every reading black-boxed to SD — zero loss, network-independent
AUTOMATIC FAIL-SAFE ROUTING
Wi-Fi / MQTT
(Primary)
ESP32 monitors link health
SX1276 LoRa
(Automatic Fallback)
Zero manual intervention required — operators keep full visibility even during a Wi-Fi outage.
BIOSENSE-EDGE | DEVS 2026
4
Notes: The methodology is closed-loop by design: sense, compute a PID correction, actuate the pumps or heater, and log to SD — all before the network is even in the picture. Connectivity is additive, not a dependency: the ESP32 continuously checks MQTT health, and if Wi-Fi drops, it silently reroutes telemetry over LoRa, so operators never lose visibility even during an outage.

## Slide 5
BOM · LOCALIZATION · FEASIBILITY · DEVS EVALUATION 20%
A 10x Cost Disruption
BIOSENSE-EDGE
₹23,000
(~$280 USD)
Fully assembled · sensor-to-cloud · locally sourced
LEGACY IMPORTED SYSTEM
₹2.5L–₹8.3L
(~$3,000–$10,000 USD)
Closed hardware · vendor lock-in · long import lead times
10x–36x
COST REDUCTION
without compromising signal isolation, precision, or fail-safe connectivity
Feasibility: Every component — MCU boards, EZO circuits, RTD driver, isolators, pumps — is available off-the-shelf in India today. No custom fab, no import wait.
github.com/GJVIJAYG/
BioSense-Edge
BIOSENSE-EDGE | DEVS 2026
5
Notes: The economics here are the real unlock. Our full BOM — every sensor, isolator, MCU, and pump — comes to twenty-three thousand rupees, against two-and-a-half to over eight lakhs for an imported system doing the same job. That's a ten-to-thirty-six times cost reduction, built entirely on locally-sourceable parts, and the full design is open-source on GitHub for any lab to replicate or extend.